## Slide 1: ROS Bootcamp
Virtualbox setup, ROS Instalation, Example applications (python), and debugging tools

## Slide 2: ROS: Overview
Robot Operating System: its not actually an operating system
Runs on top of Linux
Provides Inter-Process Communication utilities (IPC)
Makes distributed systems transparent
Is designed for robots
Notes: ROS: the Robotic Operating System, is a set of packages and tools that run on top of Linux and provide additional functionality geared towards robotics. Most of these features relate to Inter-Process Communication, the methods that different processes use to communicate with each other. Linux has built in IPC tools, but ROS adds a layer on top that makes things a little simpler. One very nice feature, is that a process does not have to know where any other nodes are running; whether or not they are on the same system makes no difference, ROS will route the messages as needed.

## Slide 3: ROS: Terminology
Node: a program
  Interacts with other nodes through topics and services
Topic: a channel for data
  Nodes can Publish messages, or Subscribe to receive them
  Think the state of some sensor
Service: a function callable by other nodes
  Request-Response
  Think ‘take an action’

## Slide 4: ROS: Terminology (cont.)
Package: A group of nodes developed together with a common theme
  Many COTS robots that run ROS put all custom nodes in one package
Namespace: A group of running nodes/topics
  Topic/Node names must be unique
  /Drive/Scaling != /Arm/Scaling
  Sort of like a folder

## Slide 5: ROS: Topics
Many-to-Many communication
Identified by unique names
Publish: To send data to all subscribers
Subscribe: To listen to messages from any Publishers
Data is passed through sockets
  ^ Implementation detail within ROS

## Slide 6: ROS: Installation

## Slide 7: Prerequisites
Python or C++ for writing nodes
Linux machine/VM preferably with Ubuntu
  ROS can also run on the Windows Subsystem for Linux (requires developer mode)
Internet Connection
Notes: We will show this with a VM

## Slide 8: Setup: VirtualBox
Install VirtualBox (virtualbox.org)
Create a new VM and select Ubuntu as the OS
Download a supported Ubuntu Image (releases.ubuntu.com/16.04/)
Go to the machine’s settings and select the image for the CD Drive
Notes: We will show this with a VM. If you do not use a supported release of ubuntu, you will need to compile ROS from source, which seems to get hairy.

## Slide 9: Setup: Installing packages
ROS: Setup Package Sources
  $ sudo sh -c 'echo "deb http://packages.ros.org/ros/ubuntu $(lsb_release -sc) main" > /etc/apt/sources.list.d/ros-latest.list’
  sudo apt-key adv --keyserver hkp://ha.pool.sks-keyservers.net:80 --recv-key 421C365BD9FF1F717815A3895523BAEEB01FA116
Load Package Lists
  $ sudo apt-get update
Notes: Lines starting with $ are to be typed at a terminal.

## Slide 10: Setup: Installing ROS
ROS: Install Core Packages/Tools
  $ sudo apt-get install ros-kinetic-desktop-full
  This will install ROS Kinetic, its utilities and debugging tools
ROSdep (dependency manager for ROS)
  $ sudo rosdep init
  $ rosdep update
Notes: Installing ROS may take a while, go grab a snack.

## Slide 11: Setup: Environment
There are some changes that need to be made to the environment variables every time you start a shell. They can be set in ~/.bashrc to take effect every time bash is launched.
  $ echo "source /opt/ros/kinetic/setup.bash" >> ~/.bashrc
To make this session work:
  $ source /opt/ros/kinetic/setup.bash
Notes: These variables basically load what packages are installed and allow tab-completion at the command line for ROS tools. Without it, ros* commands won’t work right.

## Slide 12: Setup: Workspace
Install the necessary tools for Python node development
  $ sudo apt-get install python-rosinstall python-rosinstall-generator python-wstool build-essential
Create a catkin workspace (the build system)
  $ mkdir –p ~/catkin_ws/src; cd ~/catkin_ws; catkin_make
Another setup file (specific to our own packages)
  $ source devel/setup.bash
  $ echo “source ~/catkin_ws/devel/setup.bash” >> ~/.bashrc

## Slide 13: Setup: Review
Install Ubuntu onto a VM
Update Ubuntu and install ROS packages
Setup ROS dependency manager and environment variables
Setup a catkin workspace for our code
  We didn’t actually make a package yet

## Slide 14: Creating a package
Some basic ROS nodes

## Slide 15: Package: Initialization
Make sure you are in the workspace source directory
  $ cd ~/catkin_ws/src
Make a package folder
  Our package will be called my_first_pkg, and depend on rospy (ROS Python) and std_msgs (explained later)
  $ catkin_create_pkg my_first_pkg rospy std_msgs
  The creates a folder my_first_pkg, and puts some initial data in it

## Slide 16: Package: Building
Make sure you are in the workspace root
  $ cd ~/catkin_ws/
Build the workspace
  $ catkin_make
  The builds our package(s)
Re-source the setup file
  $ source devel/setup.bash

## Slide 17: Package: Nodes
ROS systems are made of nodes that communicate through topics and services
roscore is the application that manages the connections between nodes
roscore must always be running before any nodes initialize
Let’s make a basic node now
Create a new file in my_first_pkg/src called my_first_node.py
[see next slide for the contents]

## Slide 18: Package: First Node
!/usr/bin/env python
import rospy
from std_msgs.msg import String
def talker():
pub = rospy.Publisher('chatter', String, queue_size=10)
rospy.init_node('talker')
rospy.Rate(10) # 10hz
while not rospy.is_shutdown():
hello_str = "hello world %s" % rospy.get_time()
rospy.loginfo(hello_str)
pub.publish(hello_str)
rate.sleep()
if __name__ == '__main__':
try:
talker()
except rospy.ROSInterruptException:
pass

## Slide 19: Package: Nodes
Make the file executable
  $ chmod +x <file>
Run roscore in a separate terminal
  $ roscore
Launch the node in the main terminal
  $ rosrun my_first_pkg my_first_node

## Slide 20: Package: Nodes
Open yet a third terminal
Check that the node is running, and created a topic
  $ rosnode list
  $ rostopic list
Observe the topic output (use ctrl-C to exit)
  $ rostopic echo /chatter
Observe the log messages (use ctrl-C to exit)
  $ rostopic echo /rosout

## Slide 21: Package: Nodes - Subscriber
Copy the previous node as my_second_node.py
Change the rospy.Publisher(...) line to “rospy.Subscriber(“chatter”, String, callback)” and move it below rospy.init_node(“...”)
Change the name of the node to “listener” in the init_node call
Add the following function:
def callback(data):
rospy.loginfo(rospy.get_caller_id() + "I heard %s", data.data)

## Slide 22: Package: Nodes - Subscriber
With the first node still running, use the third terminal to run the second node
Open a 4th terminal (last one) and run the same commands as before
  the new node appears, but no new topic
  You can see in the 3rd terminal that the subscriber (second node) is printing the messages from the first node.
In the 4th terminal, run the command rqt_graph
  You can see that the two nodes are connected through the chatter topic.

## Slide 23: Activity/Mini-Project
Make a loopback node

## Slide 24: Activity: Loopback node
Requirements: 2 Nodes, 2 Topics
  Node A must read messages from standard input and publish them as messages
  Node B must subscribe to messages and then publish them to another topic
  Node A subscribes to the second topic and prints the output
Try making node B do something else to the messages, like replacing keywords, or filtering